## Slide 1: Voltage regulator testing results from 2021.11.08
Goal: characterize ripple and efficiency of S-85S1AB18-I6T1U with different passive components
Sulu boards in different configurations
  DC1: Recommended 10 uF C_in, 10 uF C_out, and inductor
  DC2: Old 10 uF C_in,10 uF C_out, and old inductor from Spock
  L6 board with Sulu 10 uF C_in, 100 uF C_out, and old inductor
9 datapoints for 3 V = V_ext with no series resistance
  3 Sulu configurations
  3 resistive loads: ~0.15 mA, ~0.34 mA, and ~1.5 mA
4 datapoints for 4 V = V_ext with 1 kOhm series resistance
  DC1 and L6
Confluence page: https://crystalfree.atlassian.net/wiki/spaces/SCUM/pages/1949859841/Voltage+Regulators

## Slide 2: Testing setup

## Slide 3: Efficiency
Datasheet efficiency
Measured efficiency = (voltage out)*(current out) / [ (voltage in)*(current in) ]
DC1: Recommended 10 uF C_in, 10 uF C_out, and inductor
DC2: Old 10 uF C_in,10 uF C_out, and old inductor from Spock
L6 SCuM board with 10 uF C_in, 100 uF C_out, and old inductor
No power supply series resistance
Chart: S-85S1AB18-I6T1U with V_ext = 3 V and V_bat = 1.8 V
| 0.15270016750418761 | 0.34854666666666667 | 1.5254187604690117
DC1 | 0.8755 | 0.89515 | 0.89479
DC2 | 0.66021 | 0.66471 | 0.68805
L6 | 0.68577 | 0.67862 | 0.64883

## Slide 4: Waveforms @ 1.5 mA
  DC1: Recommended 10 uF C_in, 10 uF C_out, and inductor
DC2: Old 10 uF C_in,10 uF C_out, and old inductor from Spock
L6 board with Sulu 10 uF C_in, 100 uF C_out, and old inductor
R_load = 1.2 kOhm
V_ext = 3 V
R_ext = zero
Measured V_bat = 1.8 V

## Slide 5: Waveforms @ 0.34 mA
  DC1: Recommended 10 uF C_in, 10 uF C_out, and inductor
DC2: Old 10 uF C_in,10 uF C_out, and old inductor from Spock
L6 board with Sulu 10 uF C_in, 100 uF C_out, and old inductor
R_load = 5.3 kOhm
V_ext = 3 V
R_ext = zero
Measured V_bat = 1.8 V
Lost the .png 

## Slide 6: Waveforms @ 0.15 mA
  DC1: Recommended 10 uF C_in, 10 uF C_out, and inductor
DC2: Old 10 uF C_in,10 uF C_out, and old inductor from Spock
L6 board with Sulu 10 uF C_in, 100 uF C_out, and old inductor
R_load = 12 kOhm
V_ext = 3 V
R_ext = zero
Measured V_bat = 1.8 V

## Slide 7: Waveforms @ 1.5 mA
  DC1: Recommended 10 uF C_in, 10 uF C_out, and inductor
L6 board with Sulu 10 uF C_in, 100 uF C_out, and old inductor
R_load = 1.2 kOhm
V_ext = 4 V
R_ext = 1 kOhm
Measured V_bat = 1.5 V

## Slide 8: Waveforms @ 0.15 mA
  DC1: Recommended 10 uF C_in, 10 uF C_out, and inductor
  Measured V_bat = 1.8 V
L6 board with Sulu 10 uF C_in, 100 uF C_out, and old inductor
Measured V_bat = 1.5 V
R_load = 12 kOhm
V_ext = 4 V
R_ext = 1 kOhm

## Slide 9: Next steps
Try connecting IMU to 1.8 V DC-DC regulator
  With Spock components to identify ripple
Test traces on Sulu PCB
Spock v1.0 schematic (?)

## Slide 10: Questions
Which boards worked with the radio?
  As I recall, Sulu mostly worked, Spock 1.0 was where the ripple was noticed
Spock v1.0 schematic (?)

## Slide 11: Layout differences between Spock v1.0 and Sulu v1.0
Spock v1.0 layout (?)
Sulu v1.0 layout
cout
cin
Datasheet layout